## Slide 1: Network : Internetworking
Jae Hyeon Kim

## Slide 2: Reference
William Stalling, Data and Computer Communications 10/E, Prentice Hall

## Slide 3: Routing
Key design issue for (packet) switched networks
  Many connections will need paths more than one switch
  Select route across network between end nodes
Characteristics required
  Correctness
  Simplicity
  Robustness
  Stability
  Fairness
  Optimality
  Efficiency

## Slide 4: Performance Criteria
Used for selection of route
Approach for the optimum route
  Simplest is choose minimum hop (least number of nodes)
  Can be generalized as “least one” routing because it is more flexible, therefore it is more common than “minimum hop”
  Least-cost algorithms

## Slide 5: Example Packet Switched Network

## Slide 6: Decision Time and Place
Time
  Packet or virtual circuit basis
  Fixed or dynamically changing
Place
  Distributed routing : made by each node
    More complex, but more robust
  Centralized routing : made by some designated node
    Network control center
  Source routing : made by source station
    Allows the user to dictate a route

## Slide 7: Network Information Source and Update Timing
Routing decisions usually based on knowledge of network traffic load and link cost
  Distribute routing : using local knowledge, information from adjacent nodes, information from all nodes on a potential route
  Central routing : collect information from all nodes
Issue of update timing
  Fixed routing : never updated, simple, not sensible
  Adaptive routing : regular updates, more overload

## Slide 8: Routing Strategies (1)
Fixed routing
Use a single permanent route for each source to destination pair of nodes
The route was determined using a least cost algorithm
Route is fixed until a change in network topology : based on expected traffic or capacity
Advantage is simplicity
Disadvantage is lack of flexibility : does not react to network congestion

## Slide 9: Fixed Routing Tables

## Slide 10: Routing Strategies (2)
Flooding
Packet sent by node to every neighbor
No network information required
Eventually multiple copies arrive at destination
Each packet is uniquely numbered so duplicates can be discarded
Need to limit incessant retransmission of packets
  Node can remember identity of packet retransmitted

## Slide 11: Flooding Example

## Slide 12: Properties and Disadvantage
All possible routes are tried
  Very robust, military network
At least one packet will have taken minimum hop route
  Can be used to set up virtual circuit
Nodes directly or indirectly connected to source are visited
  Useful to distribute information
Disadvantage
  High traffic load
  Security concerns

## Slide 13: Routing Strategies (3)
Random routing
Simplicity of flooding with much less traffic load
A route node selects one outgoing path for retransmission of incoming packet
Selection can be random or round robin
A refinement is to select outgoing path based on probability calculation
No network information needed
Random route is typically neither least cost nor minimum hop

## Slide 14: Routing Strategies (4)
Adaptive routing
Used by almost all packet switching networks
Routing decisions change as conditions on the network change
Requires information about network
Disadvantages
  Decisions more complex
  Tradeoff between quality of network info. And overhead
  Reacting too quickly can cause oscillation
  Reacting too slowly means info may be irrelevant
Advantages
  Improved performance
  Aid congestion control

## Slide 15: ARPANET Routing Evolution (1)
1st generation : distance vector routing (1969)
  Distributed adaptive estimated delay, such as queue length
  Version of Bellman-Ford algorithm(doesn’t consider line speed)
2nd generation : link state routing (1979)
  Distributed adaptive using measured delay, such as RTT
  Version of Dijkstra’s algorithm
    Re-computed average delays every 10 seconds, and any changes are flooded to all other nodes
    Good under light, medium loads, but under heavy loads, little correlation between reported delays and those experienced

## Slide 16: ARPANET Routing Evolution (2)
3rd generation : link state routing (1987)
  Link cost calculation changed
    To damp routing oscillations
    To reduce routing overhead
  Measure average delay over last 10 seconds and transform into link utilization estimate
  Normalize this based on current value and previous results
  Set link cost as function of average utilization

## Slide 17: Internet Routing Protocols
Routers are responsible for receiving and forwarding packets through the interconnected set of networks Link cost
  makes routing decisions based on knowledge of the topology and traffic/delay conditions of the Internet
  routers exchange routing information using a special routing protocol
Two concepts in considering the routing function:
  routing information
    Information about the topology and delays of the Internet
  routing algorithm
    The algorithm used to make a routing decision for a particular datagram, based on current routing information

## Slide 18: Autonomous System (AS)
It exhibits the following characteristics as
  it is a set of routers and networks managed by a single organization
  consists of a group of routers exchanging information via a common routing protocol
  except in times of failure, it is connected (in a graph-theoretic sense); there is a path between any pair of nodes
Interior Router Protocol (IRP)
  a shared routing protocol which passes routing information between routers within an AS
  custom tailored to specific applications and requirements

## Slide 19: Exterior Routing Protocol (ERP)
May be more than one AS in an internetwork
  Routing algorithms and tables may differ between different AS
Routers need information about networks outside their AS
  Use an exterior router protocol (ERP) for this
  Supports summary information on AS reachability
Example
  Border gateway protocol (BGP)

## Slide 20: Application of IRP and ERP

## Slide 21: Approaches : Distance-vector Routing
Requires that each node (router or host) exchange information with its neighboring nodes
  Two nodes are said to be neighbors if they are both directly connected to the same network
First generation routing algorithm for ARPANET
  Used by Routing Information Protocol (RIP)
A node maintains a vector of link costs for each directly attached network, distance and next-hop for each destination
  Requires transmission of lots of information by each router
Changes take long time to propagate

## Slide 22: Approaches : Link-state Routing
Designed to overcome drawbacks of distance-vector
When a router is initialized, it determines the link cost on each of its network interfaces
  It then advertises this set of link costs to all other routers in the internet topology, not just neighboring routers
From then on, the router monitors its link costs
  Whenever there is a significant change, the router again advertises its set of link costs to all other routers in the configuration
The OSPF protocol is an example

## Slide 23: Consideration for ERP
Both are not effective for exterior router protocol
Not distance-vector
  Assumes routers share common distance metric
  But different Ass may have different priorities & needs
  But have no info. On AS that will be visited along a route
Not link-state
  Different Ass may use different metrics and have different restrictions
  Flooding of link state information to all routers unmanageable

## Slide 24: ERP : Path-vector Routing
Alternative to dispense with concept of routing metrics
  that is, does not include distance or cost estimate
  simply provides information about which networks can be reached by a given router and ASs crossed to get there
  so, each block of routing information lists all of the ASs visited in order to reach the destination network by this route
BGP (Border Gateway Protocol)
  it was developed for use in conjunction with the TCP/IP suite
  it has become the preferred ERP for the Internet
  designed to allow routers in different ASs to cooperate in the exchange of routing information
  current version is known as BGP-4 (RFC 4271)