## Slide 1: Network : Cellular
Jae Hyeon Kim

## Slide 2: Reference
William Stalling, Data and Computer Communications 10/E, Prentice Hall

## Slide 3: Cellular Wireless Networks
Developed to increase the capacity available for mobile radio telephone service
Key technology for mobiles, wireless networks etc.
  Based on the use of multiple low power transmitters
Area divided into cells
  In a tiling pattern to provide full coverage
  Each with own antenna, along with own range of frequencies
  Served by base station : consisting of transmitter, receiver, and control unit
  Adjacent cells re assigned different frequencies to avoid crosstalk : cells sufficiently distant can use same frequency band

## Slide 4: Cellular Geometries

## Slide 5: Frequency Reuse (1)
Object is to share nearby (but not adjacent) cell frequencies without interfering with each other
  Allows multiple simultaneous conversations with the same frequency, at the different areas
  10 to 50 channels per cell
Power of base transceiver controlled
  Allow communications within cell using a given frequency
  Limit escaping power to adjacent cells

## Slide 6: Frequency Reuse (2)

## Slide 7: Increasing Capacity (1)
Add new channels
  Not all channels used to start with
Frequency borrowing
  Taken from adjacent cells by congested cells
Cell splitting
  Use smaller cells in high use areas

## Slide 8: Increasing Capacity (2)
Cell sectoring with directional antennas
  Cell divided into wedge shaped sectors (3-6 per cell)
  Each sector is assigned a separate subset of the cell’s channels
  Directional antennas are used to focus on each sector
Microcells
  As cells become smaller, antennas move from tops of hills and large buildings to tops of small buildings and sides of large buildings
  Use reduced power to cover a much smaller area
  Good for city streets in congested areas, along highways, inside large public buildings

## Slide 9: Cellular System
Cellular system channels between mobile and base station
  Control channels : set up and maintain calls
  Traffic channels : carry voice and data

## Slide 10: Example of Cellular Call

## Slide 11: Cellular Network Generations