## Slide 1: Network : Transport Protocols
Jae Hyeon Kim

## Slide 2: Reference
William Stalling, Data and Computer Communications 10/E, Prentice Hall

## Slide 3: Transport Protocols
End-to-end transport of data that shields the user from the details of the underlying communication systems
  Reliable, connection oriented : has greater complexity, e.g. TCP
  Best effort, connectionless : datagram, e.g. UDP
Connection-oriented transport protocol mechanisms
  Provides establishment, maintenance and termination of a logical connection between TS(Transport Service) users
  Most common service for a wide variety of applications
  Is reliable, but complex

## Slide 4: Reliable Sequencing Network Service
Transport service is a simple end to end protocol between two systems on the same network
However, its situation on internet would be so complex
  Because the below layer, so IP, provide a best-effort delivery
Issues are :
  Addressing
  Multiplexing
  Flow control
  Connection establishment and termination

## Slide 5: Addressing
Transport protocol must be able to derive the following information from the TS user address
User identification
  A socket in TCP
  Port represents a particular transport service user
  Multiple users employ the same transport protocol and are distinguished by port numbers
Transport entity identification (on host)
  Specify transport protocol (TCP, UDP)
Host address of attached network device
  In the internet, a global internet address

## Slide 6: 3-layer Internet Addressing

## Slide 7: cf) Domain Name
Problem statement
  Average brain can easily remember 7 digits
  On average, IP addresses have 10.28 digits
So, we need an easier way to remember IP addresses
  Makes use of alphanumeric names to refer to hosts
  Add a distributed, hierarchical protocol (called DNS)
  Address resolution is to map between host names and IP add.
Let’s re-think our DN
  www.chonbuk.ac.kr vs www.jbnu.ac.kr

## Slide 8: Flow Control
Complex at the transport layer:
  Considerable delay in the comm. Of flow control information
  The transmission delay may be highly variable, making it difficult to effectively use a timeout mechanism for retransmission of lost data
Reasons for control:
  User of the receiving transport entity cannot keep up with the flow
  Receiving transport entity itself cannot keep up with the flow of segments

## Slide 9: Alternative to Flow Control Requirements
Do nothing
  Segments that overflow are discarded
  Sending transport entity will fail to get ACK and will retransmit
  Thus further adding to incoming data
Refuse to accept further segments from the network service
  Relies on network service to do the work
  clumsy
Use a fixed sliding widow protocol
  With a reliable network service this works quite well
Use a credit scheme
  A more effective scheme to use with an unreliable network service

## Slide 10: An Example of the Fixed Sliding Window

## Slide 11: Credit Scheme
Decouples flow control from ACK
  Then, credit scheme mainly rules the flow control
Each octet has sequence number
Each transport segment has sequence number (SN), Ack. Number (AN) and window size (W) in header
Sends sequence number of first octet in segment
ACK includes (AN=I, W=j) which means
  All octets through SN=i-1 acknowledged, want I next
  Permission to send additional window of W=j octets

## Slide 12: Sending and Receiving Perspectives

## Slide 13: Credit Allocation Mechanism

## Slide 14: Connection Establishment and Termination
Serves three main purpose:
  Allow each end to assure that the other exists, and the other’s intension to communicate with the initiator
  Allows exchange or negotiation of optional parameters
  Triggers allocation of transport entity resources
By mutual agreement

## Slide 15: Simple Connection State Diagram

## Slide 16: Connection Establishment Scenario

## Slide 17: Unreliable Network Service
More difficult case for transport protocol since
  Segments may get lost and/or arrive out of order
Examples include
  Internetwork using IP
  IEEE 802.3 with unacknowledged connectionless LLC service
Issues:
  Ordered delivery
  Retransmission strategy
  Duplication detection
  Flow control
  Connection establishment & termination
  Crash recovery