## Slide 1: Network : Transport Protocols
Jae Hyeon Kim

## Slide 2: Reference
William Stalling, Data and Computer Communications 10/E, Prentice Hall

## Slide 3: Ordered Delivery
With an unreliable network service it is possible that segments may arrive out of order
Solution is to number segments sequentially
  TCP makes use of a scheme where each data octet is implicitly numbered

## Slide 4: Retransmission Strategy
Events necessitating retransmission:
  Segment may be damaged in transit but still arrives at its dest.
  Segment fails to arrive
Sender does not know transmission was unsuccessful
Receiver acknowledges successful receipt by returning a segment containing an acknowledgement number
Retransmission strategy
  No ACK will be issued if a segment does not arrive successfully
  A timer needs to be associated with segment at it is sent
  If timer expires before acknowledgement is received, sender must retransmit

## Slide 5: Duplication Detection
Receiver received a segment, but lost its Ack.
  Eventually the sender try to retransmit the segment
  Receiver must be able to recognize duplicates
  Segment sequence numbers help
Complications arise if:
  A duplicate is received prior to the close of the connection
  Sender must not get confused if it receives multiple acknowledgements to the same segment
  Sequence number space must be long enough
  A duplicate is received after the close of the connection

## Slide 6: Incorrect Duplicate Detection

## Slide 7: Flow Control
Credit allocation quite robust with unreliable network
  Can ack data & grant credit
  Lost ACK recovers on next received
Have problem if AN=I, W=0 closing window
  Then send AN=I, W=j to reopen, but this is lost
  Sender thinks window closed, receiver thinks it open
Solution is to use persist timer
If timer expires, send something
  Could be re-transmission of previous segment

## Slide 8: Connection Establishment
Two way handshake
  A send SYN, B replies with SYN
  Lost SYN handled by re-transmission
  Ignore duplicate SYNs once connected
Lost or delayed data segments can cause connection problems
  With data segment from old connections
  Make use SYN i, where i is the sequence # of the first data
  Start segment # far removed from previous connection
  There is still a problem with SYN segment from old connections
  Need ACK to include i
  So, three way handshake

## Slide 9: Two Way Handshake problem with Obsolete Data Segment

## Slide 10: Obsolete SYN Segment

## Slide 11: Three Way Handshake : Examples

## Slide 12: TCP Entity State Diagram

## Slide 13: Connection Termination
2-way handshake is inadequate on an unreliable network
  Like connection establishment, it need 3-way handshake
Out of order segments could cause:
  The FIN segment to arrive before the last data segment
To avoid this problem the next sequence number after the last octet of data can be assigned to FIN
  Each side must explicitly acknowledge the FIN of the other using an ACK with the sequence number of the FIN to be acknowledged

## Slide 14: Failure Recovery
After restart a system, the state information of all active connections is lost
  May have half open connection because side that did not crash still thinks it is connected
Still active side of a half-open connection can close the connection using a keepalive timer
  Wait for ACK for (time out) * (number of retries)
  When expired, close connection and inform user
Or, failed side returns an RST i to every segment i that it receives
  RST i must be checked for validity on the other side
  If valid, an abnormal termination occurs

## Slide 15: TCP Services
TCP (Transmission Control Protocol) : RFC 793
  Connection oriented, reliable communication over reliable and unreliable (inter)networks
Two ways of labeling data:
  Data stream push
  User requires transmission of all data up to push flag
  Receiver will deliver in same manner
  Avoids waiting for full buffers
  Urgent data signal
  Indicates urgent data is upcoming in stream
  User decides how to handle it

## Slide 16: TCP Services Request Primitives

## Slide 17: TCP Header Format

## Slide 18: TCP Mechanisms
Can be grouped into:
connection establishment
  Always uses a three-way handshake
  Connection is determined by host and port
Data transfer
  Viewed logically as consisting of a stream of octets
  Flow control is exercised using credit allocation
Connection termination
  Each TCP user must issue a CLOSE primitive
  An abrupt termination occurs if the issues an ABORT primitive

## Slide 19: TCP Implementation Policy Options (1)
Send policy
  If no pushed data, a sending TCP entity transmits at its own convenience in credit allocation
  May construct segment per batch of data from user : quick response but higher overheads
  May wait for certain amount of data : slower response but lower overheads
Deliver policy
  In absence of push, can deliver data at own convenience
  May deliver from each segment received : higher O/S overheads but more responsive
  May buffer data from multiple segments : less O/S overheads but slower

## Slide 20: TCP Implementation Policy Options (2)
Accept policy
If segments arrive out of order the receiving TCP entity has two options:
In-order
  Accept only segments that arrive in order; any segment that arrives out of order is discarded
  Makes for simple implementation but places a burden on the networking facility
  If a single segment is lost in transit, then all subsequent segments must be retransmitted
In-window
  Accept all segments that are within the receive window
  Requires a more complex acceptance test and a more sophisticated data storage scheme

## Slide 21: TCP Implementation Policy Options (3)
Retransmit policy (three strategies)
First only
  Maintain one retransmission timer for entire queue
  If timer expires, retransmit the segment at the front of the queue
  Efficient traffic generation, but can have considerable delays
Batch
  Maintain one retransmission timer for entire queue
  If timer expires, retransmit all segments in the queue
  May result in unnecessary retransmissions

## Slide 22: TCP Implementation Policy Options (3)
Individual
  Maintain one timer for each segment in the queue
  More complex implementation

## Slide 23: TCP Implementation Policy Options (4)
Acknowledge policy (timing of ack.)
Immediate
  Immediately transmit an empty segment containing the appropriate acknowledgment number
  Simple and keeps the remote TCP fully informed
  Limits unnecessary retransmissions
  Can cause a further load on the network
Cumulative
  Wait for an outbound segment with data on which to piggyback the acknowledgement
  Typically used
  Requires more processing at the receiving end and complicates the task of estimating round-trip time

## Slide 24: UDP
Connectionless service specified in RFC 768
  Delivery & duplication control not guaranteed
Reduced overhead in transmission
Least common denominator service
Uses:
  Data collection & dissemination
  Request-response
  Real time application