## Slide 1: Network : Internet Operation
Jae Hyeon Kim

## Slide 2: Reference
William Stalling, Data and Computer Communications 10/E, Prentice Hall

## Slide 3: Internetwork Operation
Consider mechanisms for handling growth in network traffic
  from low-volume text based terminal/email
  to high volume multi-media web/voice/video
Historically, IP protocols gave best-effort datagram delivery to all services
Now, applications want variety of QoS (Quality Of Service) in IP networks
  explore some new network services and functions

## Slide 4: Multicasting
Multicast means the act of sending a packet from a source to a number of members of a multicast group
Has a number of practical applications
  multimedia “broadcast”
  teleconferencing
  database
  distributed computing
  real time workgroups
Have design issues in addressing / routing

## Slide 5: LAN Multicast
LAN multicast is easy
  send to IEEE 802 multicast MAC address
  since broadcast all stations will see packet, those in multicast group will accept it
  only single copy of packet is needed
But it is getting to be harder in internetwork environment
IP includes addresses that refer to group of hosts on one or more networks =: multicast address
  cf) IP address refers to an individual host on a particular network

## Slide 6: Multicast Example

## Slide 7: Broadcast, Multiple Unicast, Multicast
Broadcast a copy of packet to each network
  if server does not know members of group
  requires 13 copies of packet
Multiple unicast
  send packet only to networks that have hosts in group
  11 packets
True multicast
  transmit single packet along spanning tree
  routers replicate packets at branch points of spanning tree
  8 packets required

## Slide 8: Traffic Generated by Various Multicasting Strategies

## Slide 9: Requirements for Multicasting
Router have to forward more than one copy of packet
Need convention to identify multicast addresses (IPv4 Class D or IPv6 prefix)
  nodes/router translate between IP multicast addresses and list of networks containing group members
Required for hosts to join/leave multicast group
  which networks include members of given group
  sufficient info to work out shortest path to each network
Routing algorithm to calculate shortest path

## Slide 10: Internet Group Management Protocol (1)
RFC 3376 (IGMP v3) to exchange multicast group information between hosts & routers on a LAN
  hosts send messages to routers to subscribe to and unsubscribe from multicast group
  routers check which multicast groups of interest to which hosts
IGMP operation : join
  IGMP host wants to make itself known as group member to other hosts and routers on LAN
  to join, the host send IGMP membership report message
    sent in IP datagram with the multicast destination address
    the group member routers receive & learn new member

## Slide 11: Internet Group Management Protocol (2)
IGMP operation : keeping list valid
  routers periodically issue IGMP general query message
    in datagram with all-hosts multicast address
    hosts respond with report message
  router needs to know at least one group member still active
    each host in group sets timer with random delay
    if timer expires, host sends report message
IGMP operation : leave
  host leaves group by sending leave group message to all routers static multicast address
  router determines if it have any remaining group members using group-specific query message

## Slide 12: Mobile IP
Enables computers to maintain Internet connectivity while moving from one Internet attachment point to another
Particularly suited for wireless connections
mobile implies:
  a user is connected to one or more applications across the Internet
  the user’s point of attachment changes dynamically
  all connections are automatically maintained despite the change of attachment

## Slide 13: Basic Capabilities of Mobile IP
Network discovery
  used to identify prospective foreign agents, by means of beacon
  then a care-of address is dynamically acquired for a temporary IP address of current network
New address registration
  the care-of address must be registered to home agent in order to redirect datagram reached to home to the foreign agent
  authenticated registration procedure is used
Datagram tunneling
  forwards IP datagram from a home address to a care-of address

## Slide 14: Mobile IP Scenario

## Slide 15: Internetwork Quality of Service
Internet traffic continues to grow and change
  demand for real-time responses
  increasing use of audio, image, and video
  heavy use of the World Wide Web
Packet-switching technology with routers functioning as switches was not designed to handle voice and video
  strong need to support a variety of traffic with QoS requirements within TCP/IP

## Slide 16: Internet Traffic Categories
Elastic traffic
  can cope with wide changes in delay and/or throughput
  traditional TCP/IP traffic
    eg. FTP, email, telnet, SNMP, HTTP
Inelastic traffic
  does not easily adapt to network variations, e.g. real time traffic
  requirements : throughput, delay, jitter, packet loss
New Internet architecture requirements:
  resource reservation protocol
  elastic traffic still needs to be supported

## Slide 17: ISA Approach
Integrated Service Architecture (ISA)
  intended to provide QoS transport over IP-based Internet
  defined in RFC 1633
  portions already being implemented in some routers
  sharing capacity on congestion is the central design issue
To manage congestion and provide QoS, it makes use of:
  admission control
  routing algorithm
  queuing discipline
  discard policy

## Slide 18: ISA Services
ISA service for a flow of packets is defined on two levels:
  a number of general categories of service are provided, each of which provides a certain general type of service guarantees
    guaranteed : service provides assured capacity
    controlled load : tightly approximates the behavior visible to applications
    best effort
  within each category, the service for a particular flow is specified by the values of certain parameters
    referred to as a traffic specification (TSpec)

## Slide 19: Resource Reservation: RSVP
Resource ReSerVation Protocol : RFC 2205
  provides supporting functionality for ISA
Applications reserves resources in-between routers to meet QoS
  enables routers to decide ahead of time if they can meet the delivery requirement for a multicast transmission
Goals and characteristics
  unicast and multicast
  receiver-initiated reservation
    maintaining soft state in the Internet
  providing different reservation styles
    transparent operation through non-RSVP routers

## Slide 20: Receiver-Initiated Reservation
Since receivers specify the desired QoS, it makes sense for them to make resource reservations
  different members of the same multicast group may have different resource requirements
  QoS requirements may differ depending on the output equipment, processing power, and link speed of the receiver
  routers can aggregate multicast resource reservations to take advantage of shared path segments

## Slide 21: RSVP Operation

## Slide 22: Differentiated Services (DS)
ISA and RSVP are relatively complex to deploy
Designed to provide simple, low overhead tool
  specified in RFC 2475
  IP packets labeled for differing QoS using existing IPv4 Type of Service or IPv6 DS field, so no change to IP is required
Key characteristics:
  SLA(Service Level Agreement) is established prior to use of DS
  DS is implemented in individual routers
  most widely accepted QoS in enterprise networks

## Slide 23: DS Field IPv6