## Slide 1: Network : Congestion Control
Jae Hyeon Kim

## Slide 2: Reference
William Stalling, Data and Computer Communications 10/E, Prentice Hall

## Slide 3: Congestion Control
Congestion occurs when the number of packets being transmitted through the network approaches the packet handling capacity of the network
  Congestion control aims to keep number of packets below level at which performance falls of dramatically
Data network is a network of queues
  Generally 80% utilization is critical
Finite queues mean data may be lost

## Slide 4: Finite Queues
Queue at a node
Interaction of queues

## Slide 5: Effects of Congestion
What typical works on a router
  Packets arriving are stored at input buffers
  Routing decision made
  Packet move to output buffer
Packets queued for output transmitted as fast as possible
  Statistical time division multiplexing
If packets arrive to fast to be routed, or to be output, buffers will fill
  Can discard packets
  Can use flow control : propagate congestion though network

## Slide 6: Idel vs. Practical Performance
Practical performance
  Ideal assumes infinite buffers and no overhead
  But, buffers are finite
  Overheads occur in exchanging control msgs
Effects of congestion
  With no control

## Slide 7: Mechanisms for Congestion Control

## Slide 8: Backpressure
If a node becomes congested it can slow down or halt flow of packets from other nodes
  Then, other nodes have to apply control on incoming packet rates
  Flow restriction propagates backward to sources, which are restricted in the flow of new packets into the network
Can be exerted on the basis on links or logical connections
  Can be selectively applied to logical connections so that the flow from one node to the next is only restricted on some connections
Only recently developed for IP

## Slide 9: Choke Packet
Control packet
  Generated at congested node
  Sent to source node
An example is Internet Control Message Protocol (ICMP) source quench packet
  From router or destination end system
  Source cuts back until it no longer receives quench messages
  Message is issued for every discarded packet
  Message may also be issued for anticipated congestion
Crude control technique

## Slide 10: Congestion Signaling
Implicit congestion signaling
  With network congestion, transmission delay increases, and/or packets may be discarded
  Source can detect congestion and reduce flow
  Effective on connectionless (datagram) networks
Explicit congestion signaling
  Network alerts end systems of increasing congestion
  End systems take steps to reduce offered load
  Backwards : congestion avoidance in opposite direction
  Forwards : congestion avoidance in same direction

## Slide 11: Explicit Signaling Categories
Binary
  A bit set in a packet indicates congestion
Credit based
  Indicates how many packets source may send
  Common for end to end flow control
Rate based
  Supply explicit data rate limit
  Nodes along path may request rate reduction

## Slide 12: Traffic Management
Fairness
  Provide equal treatment of various flows
Quality of Service (QoS)
  Different treatment for different connections
Reservations
  Traffic contract between user and network
  Excess traffic discarded or handled on a best-effort basis

## Slide 13: Congestion Control in Packet Switched Networks
Send control packet to some or all source nodes
  Requires additional traffic during congestion
Rely on routing information
  May react too quickly
End to end probe packets
  Adds to overhead
Add congestion info. To packets as they cross nodes
  Either backwards or forwards
So, two categories of TCP congestion control
  Retransmission timer management
  Window management

## Slide 14: Retransmission Timer Management (1)
As network conditions change, a static retransmission timer is likely to be either too long or too short
  All TCP attempt to estimate the current round-trip time and then set the timer to a value somewhat greater than the estimated time
  Simple average
  Exponential average : RFC 793

## Slide 15: Retransmission Timer Management (2)
Jacobson’s algorithm
  RTT exhibits a relatively high variance
  With low variance of RTT, RTO is too high, whilst in an unstable environment, β = 2 may be inadequate with unnecessary retrans.
  Again, give greater weight to more recent instances because they are more likely to reflect future behavior

## Slide 16: Jacobson’s RTO Calculation

## Slide 17: Exponential RTO Backoff
When a TCP sender times out on a segment, it must retransmit that segment
  Timeout probably due to congestion, such as dropped packet or long round trip time
Hence, maintaining the same RTO is not good idea
A more sensible policy dictates that a sending TCP entity increase its RTO each time a segment is re-transmitted

## Slide 18: Karn’s Algorithm
If a segment is re-transmitted, the ACK arriving may be:
  For the first copy of the segment (RTT longer than expected)
  For second copy
No way to tell for which one
Do not measure RTT for re-transmitted segments
But calculate backoff when re-transmission occurs
Use the backoff RTO until ACK arrives for segment that has not been re-transmitted

## Slide 19: Window Management (1)
The size of sending window can have a critical effect on TCP performance in front of a congestion
Slow start : gradually expanding the window
  awnd = MIN[credit, cwnd]
  Start connection with cwnd = 1
  Increment cwnd by 1 (actually 2) at each ACK, to some max

## Slide 20: Window Management (2)
Dynamic windows sizing on congestion
  Jacobson points out that “it is easy to drive a network into saturation but hard for the net to recover”
  With the slow start, cwnd keeps growing exponential until it becomes equal to receiver window (credit)
  However, for the congestion, the exponential growth of cwnd may be too aggressive and may worsen the congestion

## Slide 21: Illustration of Slow Start and Congestion Avoidance

## Slide 22: Implementation of TCP Congestion Control Measures