## Slide 1: Network : Protocol
Jae Hyeon Kim

## Slide 2: Reference
William Stalling, Data and Computer Communications 10/E, Prentice Hall

## Slide 3: Protocol Architecture
Need for protocol architecture to transfer data several tasks must be performed
  The source must activate communications path or inform network of the identity of the desired destination
  The source must make sure that dest. Is prepared to receive data
  The file transfer application on source must confirm file mgmt program at destination is prepared to accept and store the file
  A format translation function may need to be performed if the formats used on the two systems are different

## Slide 4: Function of Protocol Architecture
Breaks logic into subtask modules
Modules are arranged in a vertical stack, so layering
  Each layer in the stack performs a subset of functions
  Relies on next lower layer for primitive functions
  Provides services to the next higher layer
  Changes in one layer should not require changes in other layers
A protocol is a set of rules or conventions that allow peer layers to communicate, the key features of a protocol are:
  Syntax : format of data blocks
  Semantics : control information for coordination
  Timing : speed matching and sequencing

## Slide 5: Communication Layer
Communication tasks are organized into three relatively independent layers:
  Application layer : contains logic to support applications
  Transport layer : provides reliable data transfer
  Network access layer : concerned with the exchange of data between a computer and the network to which it is attached

## Slide 6: Protocol Architecture and Networks

## Slide 7: Protocol in a Simplified Architecture

## Slide 8: Standardized Protocol Architectures
Required for devices to communicate
Vendors have more marketable products
Customers can insist on standards based equipment
Two standards:
  OSI reference model : never lived up to early promises
  TCP/IP protocol suite : most widely used
Also : IBM System Network Architecture(SNA)

## Slide 9: OSI Reference Model

## Slide 10: TCP/IP Layers and Example Protocols
Dominant commercial protocol architecture
  Specified and extensively used before OSI
No official model but a working one

## Slide 11: Operation of TCP/IP

## Slide 12: Some Protocols in TCP/IP Suite

## Slide 13: Standards
Required to allow for interoperability between equipment
  De facto standards e.g.) UNIX, IBM PC, Windows
  De jure standards e.g.) OSI 7 layers
Advantages
  Ensures a large market for equipment and software
  Allows products from different vendors to communicate
Disadvantages
  Freeze technology
  May be multiple standards for the same thing
Web sites for IETF, IEEE, ITU-T, ISO

## Slide 14: Socket Programming
Concept was developed in the 1980s in the UNIX environment as the Berkeley sockets interface
  De facto standard application programming interface (API)
  Basis for Window Sockets (WinSock)
Enables communications between a client and server process
It may be connections oriented or connectionless
TCP/UDP header includes source port and dest. Port
  These port values identify the respective users(applications) while the IP addresses identify the respective host systems

## Slide 15: The Socket
Formed by concatenating a port value and an IP address
  Unique throughout the Internet
Used to define a communication API
  Generic interface for writing programs that use TCP or UDP
Socket parameters
  domain {AFUNIX, AF_INET, AF_INET6}
  Type {stream, datagram, raw}
  Protocol {TCP, UDP, ICMP}
Socket data structure depends on the implementation
Cf) reserved port ≈ well-known port ≈ server port

## Slide 16: Core Socket Functions

## Slide 17: Socket System Calls for Connection-oriented Protocol

## Slide 18: Skeleton of Client/Server Programming

## Slide 19: Client/Server Operational View