## Slide 1: Network : Wide Area Networks
Jae Hyeon Kim

## Slide 2: Reference
William Stalling, Data and Computer Communications 10/E, Prentice Hall

## Slide 3: WAN Technology and Protocols
Switched communications networks
  Switching nodes : provide a switching facility that move data between nodes
  Stations : devices attached to the network
  Nodes : switching devices that provide communication
  Communications network : collection of nodes
  Switched network : data entering the network from a station are routed to the destination by being switched from node to node

## Slide 4: Circuit Switching
Uses a dedicated path between two stations
Has three phases
  Establish
  Transfer
  disconnect
Inefficient
  Channel capacity dedicated for duration of connection
  If no data, capacity wasted
Set up (connection) takes time
Once connected, transfer is transparent

## Slide 5: Public Circuit Switched Network

## Slide 6: Circuit-Switching Technology
Driven by application that handle voice traffic
  Key requirements is no transmission delay and no variation in delay
  Efficient for analog trans. Of voice signals but, inefficient for digital trans.
Transparent
  Once a circuit is established, it appears as a direct connection no special logic is needed
Telecommunication components
  Subscriber : devices attached to network
  Local loop : subscriber loop
  Exchange : switching centers
  Trunks : branched between exchanges

## Slide 7: Circuit Switch Elements
Circuit establishment
Circuit switch elements

## Slide 8: Blocking or Non-blocking
Blocking network
  May be unable to connect stations because all paths are in use
  Used on voice systems because it is expected to be of short duration and that a fraction of the phoned will be engaged at any one time
Non-blocking network
  Permits all stations to connect at once
  Grants all possible connection requests as long as the called party is free
  On using data connections, terminals can be continuously connected for long periods of time so nonblocking configurations are required

## Slide 9: Space Division Switching
Originally developed for analog environment
  Signal paths are physically separate from one another
Crossbar switch
  Number of crosspoints grows as square of number of stations
  Loss of crosspoint prevents connection
  Inefficient : all stations connected, only a few crosspoints in use
Multistage switch
  Reduced number of crosspoints
  More than one path through network, so increased reliability
  More complex control
  May be blocking

## Slide 10: Crossbar Matrix

## Slide 11: Three Stage Space-Division Switch

## Slide 12: Packet Switching
While circuit switching was designed for voice, packet switching was designed for data
Transmitted in small packets
  Packets contains user data and control information
  Packets are received, stored and past on to the next node

## Slide 13: Advantages
Line efficiency
  Single link is shared by many packets over time
  Packets queues and transmitted as fast as possible
Data rate conversion
  Each station connects to the local node at proper speed
  Nodes buffer data if required to equalize rates
No blocking of calls
  Packets are accepted even when network is busy
  Delivery may slow down – delivery delay increases
Priorities can be used

## Slide 14: Switching Technique
Station breaks long message into packets
Packets sent one at a time to the network
Packets handled in two ways
  Datagram : each packet is treated independently with no reference to previous packets
  Virtual circuit : a preplanned route is established before any packets are sent

## Slide 15: Datagram Approach

## Slide 16: Virtual Circuit Approach

## Slide 17: Virtual Circuits vs. Datagram
Virtual circuits
  Network can provide sequencing and error control
  Packets are forwarded more quickly (no routing decisions to make)
  Less reliable (failure of a node lose all circuits through that node)
Datagram
  No call setup phase (better if few packets)
  More flexible (routing can be used to avoid congested parts of the network)
  More reliable (if a node fails, find an alternate route)

## Slide 18: Event Timing

## Slide 19: Effect of Packet Size
There is a significant relationship between packet size and transmission time
  data pass through X to Y,
  packet size 43 octets (40 data, 3 control)