## Slide 1: Network : Internet Protocol (2)
Jae Hyeon Kim

## Slide 2: Reference
William Stalling, Data and Computer Communications 10/E, Prentice Hall

## Slide 3: Internet Protocol

## Slide 4: TCP/IP Concepts

## Slide 5: Connectionless Operation
Internetworking involves connectionless operation at the level of the Internet Protocol
IP provides a connectionless service
  Initially developed for the DARPA Internet project
  Protocol is needed to access a particular network
Connectionless Internet facility
  Is flexible
  Can be made robust
  Does not impose unnecessary overhead

## Slide 6: IP Operation

## Slide 7: IP Design Issues
Routing
Datagram lifetime
Fragmentation and reassembly
Error control
Flow control

## Slide 8: Routing
ES/router maintain routing tables
  The table indicate next to which datagram is sent
  It can be static or dynamic
Router decides the next router to which the internet datagram should be sent : see next in detail
  Source routing : source specifies route to be followed and can be useful for security and priority
  Route recording : each router appends its Internet address to a list of addresses in the datagram, useful for testing and debugging

## Slide 9: Datagram Lifetime
Datagrams could loop indefinitely, possibly with making use of incorrect routing information
  Consumes resources
  IP may need upper bound on lifetime of a datagram
IP lifetime
  Specified in lifetime, so Time to Live (8 bits), TTL in IP header
  Initially, it is assigned in the sender’s OS, as 64 or 128
  Every router that processes a datagram must decreases the TTL by at least one, so the TTL is similar to a hop count
  In addition, the router decrease the time, in seconds, that a datagram is stayed in the router

## Slide 10: Fragmentation and Re-assembly (1)
Lower-level protocols may need to break data up into smaller blocks, called fragmentation
Reasons for fragmentation
  Network only accepts blocks of a certain size
  More efficient error control & smaller retransmission units
  Fairer access to shared facilities
  Smaller buffers
Disadvantages
  Greater overhead with more percentage of control information
  More interrupts & processing time

## Slide 11: Fragmentation and Re-assembly (2)
Issue of when to re-assemble
  At destination : packet get smaller ad data traverses Internet
  At intermediate node (router) : need large buffers at routers, buffer may fill with fragments, all fragments must go through same router

## Slide 12: IP Fragmentation
IP re-assembles at destination only
Make use of fields in header
  Data unit identifier (ID) : identifies end system originated datagram
  Data length : length of user data in octets
  Offset : position of fragment of user data in original datagram
  More flag : indicates that this is not the last fragment

## Slide 13: Fragmentation Example

## Slide 14: Error and Flow Control
Error control
  Discarded datagram
  So, identification is needed
  Reasons for discarded datagrams include : lifetime expiration, congestion, FCS error
Flow control
  Allows routers to limit the rate they receive data
  Send flow control packets requesting reduced data flow
Error and flow control takes place in station to station
  That is, TCP have the role

## Slide 15: Internet Protocol (IP) v4
IPv4 is defined in RFC 791 as a part of TCP/IP suite
It consists of two parts
  Specification of interface with a higher layer
  Specification of actual protocol format and mechanisms
IP services
  Primitives : specifies functions to be performed, the actual form of a primitive is implementation dependent
  Parameters : used to pass data and control information

## Slide 16: IP Parameters
Source address and destination address
Protocol
Type of Service
Identification
Fragment indicator {More bit | Don’t fragment bit}
Time to live
Data length
Option data (security, source routing, route recording, stream identification..)
User data

## Slide 17: IPv4 Header

## Slide 18: IPv4 Address Formats

## Slide 19: IP Addresses
Class A
  Start with binary 0, range 1.x.x.x to 126.x.x.x
  All 0 reserved, 01111111 (127) reserved for loopback
Class B
  Start with binary 10, range 128.x.x.x to 191.x.x.x
Class C
  Start with binary 110, range 192.x.x.x to 223.x.x.x
Private address (vs. public address)
  Range as 10.x.x.x, 172.16.x.x, 192.168.x.x
  Mapped by a Network Address Translation (NAT) box