## Slide 1: Network : Internet Protocol (2)
Jae Hyeon Kim

## Slide 2: Reference
William Stalling, Data and Computer Communications 10/E, Prentice Hall

## Slide 3: Subnets and Subnet Masks
Aims to save the IP addresses by sharing an address with a set of physical networks
Allows arbitrary complexity within an organization
  Insulate overall Internet from growth of network numbers and routing complexity
  Site looks to rest of internet like single network
Each LAN assigned subnet number
  Host portion of address partitioned into subnet # and host #
  Local routers route within subnetted network
Subnet mask indicates which bits are subnet number and which are host number

## Slide 4: IP Addresses and Subnet Masks

## Slide 5: An Example : Routing Using Subnets

## Slide 6: Mapping IP Addresses to the DL
Consider an Ethernet(IEEE802.3) LAN running IP
  Recall data link layer has it’s own 48-bit addresses
  Network layer provide it’s own 32-bit IP address space
  Data link layer knows nothing about IP addresses
How do these two sets of addresses get mapped?
  ARP(Address Resolution Protocol, RFC 826) build a query message and broadcast it
  All hosts in the network receive it and one says “that’s me!”

## Slide 7: Address Resolution Protocol (ARP)
ARP is a part of the physical network system
  But it is not a part of the IP
ARP is a low-level protocol that hides the underlying network physical addressing
  And permits a machine to assign an arbitrary IP address
Now, the broadcasting is too expensive, how can it be solved?
  When a host receives an ARP reply, it saves the sender’s IP address and its physical address in its cache for successive lookups
Is it be possible more refinement?
  The sender’s IP-to-physical address binding is included in every ARP broadcast; receivers update the binding in their cache

## Slide 8: Table Driven IP Routing
IP routing employs an routing table on host and router
  The routing table contains information about the possible destinations and how to reach them
  IP consults the table to decide where to send the datagram
Then, what information should be kept in routing tables?
  Minimal information principle : keep network prefix only
  Information hiding principle : specifies one step along the path from the router to a destination
  Default routing : if no route appears in the table, the routing routines send the datagram to a default router

## Slide 9: Table Driven IP Routing (An Example)

## Slide 10: Routing Protocols in IPv4
IP routing is based on the destination network ID alone?
  All IP traffic for a given network tales the same path regardless to the delay or throughput of physical network
  Only the final router can determine if the destination exists or is operational, the router only can report the delivery to the sender
  Each router routes traffic independently – someone should find out if two-way communication is always possible
IP routing selects the next hop to be sent the datagram
  IP simply passes the datagram and the next hop IP address to the network interface software (so-called network driver)
  The driver software responsible to bind the next hop IP address to a physical address, forms a frame, and sends it

## Slide 11: Internet Control Message Protocol (ICMP)
RFC 792
Provides a means for transferring message from routers and other hosts to a host
Mainly provides feedback about problems
  Datagram cannot reach its destination
  Router does not have buffer capacity to forward
  Router can send traffic on a shorter route
Encapsulated in IP datagram
  Hence net reliable

## Slide 12: ICMP Message Format

## Slide 13: Why Change IP?
Address space exhaustion
  Two level addressing (network and host) wastes space
  Network addresses used even if not connected to Internet
  Growth of networks and the Internet
  Single address per host
Requirement for new types of service
  Address configuration
  Routing flexibility
  Traffic support
Security
mobility

## Slide 14: IPv6 RFCs
IP versions
  IP v1-3 defined and replaced
  IP v4 - current version
  IP v5 - streams protocol
  IP v6 - replacement for IP v4 : during development it was called IPng(IP Next Generation)
RFC 1752 – recommendations for the IPng
  Requirements
  Addressing, routing security issues
RFC 2460 – overall specification
RFC 4291 – addressing structure

## Slide 15: IPv6 Enhancements
Expanded address space
  128 bit
Improved option mechanism
  Separate optional headers between IPv6 header and transport layer header (most are not examined by intermediate routes)
Dynamic address assignment
Increased addressing flexibility
  Anycast – delivered to one of a set of nodes
Support for resource allocation
  Labeling of packets to particular traffic flow

## Slide 16: IPv6 Packet with Extension Headers

## Slide 17: IPv6 Header

## Slide 18: IPv6 Flow Label
Related sequence of packets
  Needs a special handling for a specific packet
  Identified by source and destination address + flow label
Router treats flow as sharing attributes
  E.g. path, resource allocation, discard requirements, security
May treat flows differently
  Buffer sizes, different forwarding precedence, different QoS
Flow requirements are defined prior to flow start and a unique flow level is assigned to the flow
  Alternative to including all info in every header

## Slide 19: Next Header

## Slide 20: IPv6 Addresses
128 bits long
Assigned to an interface rather than a host
  Single interface may have multiple unicast addresses
Three types of address
  Unicast : single interface
  Anycast : set of interfaces (typically different nodes), delivered to any one interface, usually the “nearest”
  Multicast : set of interfaces, delivered to all interfaces identified

## Slide 21: Extension Headers
Hop-by-hop options
  Require processing at each router
Routing options
  Similar to v4 source routing
Fragmentation options
  Only allowed at source, no fragmentation at intermediate routers
Authentication options
  Encapsulating security payload
Destination options
  Carries optional information for destination node

## Slide 22: IPv6 Extension Headers

## Slide 23: Virtual Private Network (VPN)
Set of computers interconnected using an unsecure network, as Internet
  But they provide a secure channel between the organizations, much like as a private network
Using encryption & special protocols to provide security
  Eavesdropping (cryptography)
  Entry point for unauthorized users (authentication)
Proprietary solutions are problematical
  Hence, develop the IPSec standard

## Slide 24: IPSEC
RFC 1636 (1994) identified security need
Encryption & authentication to be IPv6
  But designed also for use with current IPv4
Applications needing security include:
  Branch office connectivity
  Electronic commerce security
Benefits
  Provides strong security for external traffic
  Resistant to bypass
  Can be transparent to applications as well as end users

## Slide 25: IPSEC Function
Authentication header
  For authentication only
Encapsulating Security Payload (ESP)
  For combined authentication/encryption
A key exchange function
  Manual or automated
VPNs usually need combined functions

## Slide 26: IPSEC Scenario : VPN